Document Camera

Link to our website with short training video clips showing how to connect document camera, using the remote, capturing pictures etc.

http://ittwiki.northstar.k12.ak.us/4._Resources/Document_Camera

When you want to be able to easily switch  between projecting what is on your computer AND what is under the Document camera use the following chord set-up.

1st Chord- connect the computer (using your dongle) with VGA IN on the Document camera.

2nd chord- connect OUT from Document Camera  to IN on the Projector.

You can toggle between the two by clicking on the PC and Camera buttons on the top of the Document Camera.

***You may need to click Detect Displays on your laptop (under system preferences( Displays  or on your menu bar if you put the Display icon there) when you want to switch between the two.

Another tip:  Be sure the tiny little black toggle on the side of the Document camera is switched to RGB and NOT TV

Troubleshooting a  frozen document camera

This tip is from Avermedia "Live Chat" www.avermedia-usa.com

Here are the steps

1. Plug document camera into a projector using the VGA cord (not USB)

2. If image is flashing - Press the Freeze button on the Document Camera

3. Press the Menu button

4. On the screen select "Default"

5. On the screen select "Yes"

6. Unplug for at least 5 seconds.

7. Plug back in and it works.